Pedicure Chair Installation Guide

- Start by first removing the Seat Frame from the box and placing it on the base.    Secure the seat frame with four bolts.

- Install the actuators according to the actuator installation guide provided.

- With a flat head screwdriver remove the plastic cap A on the seat frame (Seat).  Then with a 1/8th inch allen wrench, loosen Pin B under the plastic cap (Do not remove the pin completely).  Then slide Bolt C out so that it is flush with the frame. Repeat this step for the other side of the seat frame.

- The next step will require two (perhaps three) people.  Remove the back of the chair (Back) from the box.  Align the holes on the side of the Back with Bolt C.  Slide Bolt C into the Back and tighten Pin B to lock Bolt C into place. Repeat this step for the other side of the seat frame.

- Now we will install the armrests.  Remove the armrests from the box.  Depending on the armrest you will need to either unzip the cover to expose the mounting hole (18, 28, 68 series) or remove a plastic cover (38 series)  Next remove the hex nut on Bolt D and place the Armrest onto Bolt D.  Tighten the Hex Nut to Secure the Armrest. Then hide the mounting holes to

- Now you will secure the Back to the bottom actuator.  Start by removing the lock pin and mounting pin from the actuator that attaches to the bottom of the back.  Then position the back

- Use a pair of scissors to cut the shrink-wrap covering on the seat massage connectors, making sure not to cut the wires in the process.  Depending on whether you have an Air Seat or Vibration Seat, either connect the air seat connector to the air pump and the air pump to the seat cushion or connect the vibration seat connector to the wire from the seat cushion.

- The next step will be to place the seat cushion onto the seat frame and fasten the wing nuts.  Then place the back cushion and pillow into the chair.

- Finally plug the chair into the outlet and turn on the power on the left side of the Back.

# Text boxes

Cap A

Bolt C

Pin B

Bolt D